## Slide 1: Manufacturing the mini grubbing hoe
Making a Jig for Production

## Slide 3: Making a prototype
Making a prototype will help identify problems that can be solved using jigs and templates.

## Slide 4: Make a template
Refine your design and cut a template for the hoe end of the mini grubbing hoe

## Slide 5: Make each piece uniform
Use the template to draw each piece so they will be cute to a uniform size and shape

## Slide 6: Create a jig
Use your template to create a jig to bend your fork ends.
Note: this jig will need to be smaller than the template if you want the same size fork as the hoe end.

## Slide 7: Calculate fork length
Calculate how long to cut the pieces to make the ends of the fork even once they are bent.

## Slide 8: Ready for a vise
Attach a flat bar to the bottom of your jig.
This allows you to hold the jig in a vise while you are bending or welding.

## Slide 9: Prepare the forks
Use the grinder to sharpen both ends of the fork piece.
Heat the fork piece with the oxy fuel torch and bend the fork.

## Slide 10: Making a fork jig
Use a fork bend to make the fork end jig.
Weld small pieces of bar stock to hold fork in place.

## Slide 11: Jig for the center fork
Add a third piece to align the center fork for welding.

## Slide 12: Adding a stop to the jig
Add a forth piece to act as a stop for the fork and to center the square tubing for welding.

## Slide 13: Putting the pieces together
Using the jig to help hold the pieces then tack weld your pieces together.

## Slide 14: Check for fit
Remove the tool from the jig to check for fit.
Make adjustments as needed.
Weld your pieces together on both sides.

## Slide 15: Finishing
Clean with a flap disk or die grinder.
Prime and paint

## Slide 16: Fitting the handle
Cut handle a little longer than the tubing used.
Use handsaw to make stopping cuts.
Use a knife or chisel to spit the chips off, so the handle will fit into the tubing.

## Slide 17: Finishing the handle
Saw a slit into the end of the handle and cut a wedge to drive in the slit.
Fit the handle just as you would put any handle on.
Coat handle with a clear finish.